## Slide 1: FS Laser Operation-Draft 1
Weston Middle School

## Slide 2: Log In to Computer
Turn on the PC power switch and screen power
Allow to boot up( 3 min)
Ctrl-Alt-Delete
Log in with Weston username and password

## Slide 3: Upload files to Desktop
Plug in flash drive, drag SVG files onto desktop

## Slide 4: Launch Programs
Programs- Retina Engrave
Programs- Corel Draw

## Slide 5: Turn on Laser System
Turn on wall power switch; chiller, compressor, and blower should start up
Chiller Temp should read 21-22 degrees C
Turn on Key Switch on Laser
Pull out Laser Power switch

## Slide 6: Wait for Laser to Boot Up

## Slide 7: Once Laser has booted up….
Refresh connection in lower-left of Retina Engrave; wait for green “connected” message

## Slide 8: Adjust Z-Axis focus
Insert material onto honeycomb tray
Press Mode switch( left switch) until display says “Fast Z”
Using up+down arrow buttons, adjust height so auto-focus switch just touches stock

## Slide 9: Homing
Set Mode Switch to “Fast X-Y”
Press “Home” switch( house)
Laser should home to top right corner of bed

## Slide 10: Adjust laser position
In “Fast X-Y” mode, use arrow keys to move laser to top left corner of etch area

## Slide 11: Load Image into Corel Draw
In Corel Draw—Do File—Open- browse to SVG file on desktop-open file
Scale image to correct size

## Slide 12: Print- Part 1
When image is correct size, do File-Print with CorelDraw—Select “Full Spectrum Engineering Driver”

## Slide 13: Open Retina Engrave
Image should open in Retina Engrave
For Vector Cut:
  Select Vector Tab
  Adjust Vector power—
    15% for cutting thin material
    60% for ¼” maple
    12% for vector engrave of wood

## Slide 14: Set Power

## Slide 15: Check Perimeter
Push Perimeter button to see etch area
Adjust position with arrow keys

## Slide 16: Run Job
Click on Green Arrow in Retina Engrave; job should start

## Slide 17: Do Not run laser unattended!
When job finishes, open door and remove material
Shut off laser
Shut down wall power